122	5

TRANSISTORS ● AF PERFORMANCE
KD 501, KD 502, KD 503	NPN – FOR LINEAR APPLICATIONS
NPN – TPAHЗИCTOPЫ ДЛЯ ЛИHEЙHЫX CХEM ● NPN – TRANSISTOR FOR LINEAR CIRCUITS ● NPN TRANSISTOREN FÜR LINEARANWENDUNGEN
NPN silicon transistors, with a power dissipation of 150 W, made by MESA technology with an epitaxial base, suitable for the output stages of low-frequency amplifiers.
Metal case with two glass isolated passages for base and emitter.
The collector is conductively connected to the housing.
Weight: max. 25 g.
•) For sockets covered with solder,
    max. 1,8 mm.
••) It is measured at a distance of
    max. 1.5 mm from the case.
Absolute max limits:	Tc = +25 °C
Collector-emitter voltage KD 501 / KD 502 / KD 503	UCEO / UCEO / UCEO	max. / max. / max.	40 / 60 / 80	V / V / V
Collector-emitter voltage KD 501 / RBE = 47 Ω KD 502 / KD 503	UCER / UCER / UCER	max. / max. / max.	50 / 70 / 90	V / V / V
Emitter – Base Voltage	UEBO	max.	5
Collector Current (DC)	IC	max.	20	V
Collector Current Impulse	ICM	max.	30	V
Base Current (DC)	IB	max.	7	A
Total Power Dissipation 1)	Ptot	max.	150	W
Thermal Resistance, Junction−to−Case	Rthjc	max.	0,866	K/W
Operating Junction Temperature Range	Tj	max.	155	°C
Storage Junction Temperature Range	Tstg	max.	–50 ... +50	°C

1) The maximum Total Power Dissipation is precisely defined, meaning at UCE = 30 V, TC = 100 °C and PC = 65 W, no second breakdown must be allowed to occur.

Characteristic data:	Tc = +25 °C
Nominal values:		min.–max.
Collector-emitter voltage / (IC = 0,2 Ω) KD 501 / KD 502 / KD 503	UCEO / UCEO / UCEO	≥40 / ≥60 / ≥80	V / V / V
Collector-emitter current / UCE = 50 V, RBE = 47 Ω KD 501 / UCE = 70 V, RBE = 47 Ω KD 502 / UCE = 90 V, RBE = 47 Ω KD 503	ICER / ICER / ICER	≤10 / ≤10 / ≤10	mA / mA / mA
Collector saturation voltage / (IC = 10 A, IB = 1 A)	UCE sat	≤0,75	V

Note: This translation is based on a direct transcript of the original Czech datasheet. Shown on the next pages are this original datasheet and the initial transcript. Further note that this translation has been done with translation tools and the sole purpose of the transcript is to ease any future translation efforts. This transcript and translation does not imply any IP-rights on my behalf, I’ve not done any more that actually transcribe and translate the original document, recreating some graphical elements in the process. So, nothing much really.
Cheers!
Gjermund Skogstad
Norway