322	5

TRANSISTORS ● LOW AND MEDIUM PERFORMANCE SWITCHES
––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––––
KU 607, KU 608 NPN – FOR SWITCHING AND REGULATORY APPLICATIONS
NPN – TPAHЗИCTOP ДЛЯ ПEPEKЛЮЧAЮЩИX И УПPABЛЯЮЩИX CXEM ● NPN – TRANSISTOR FOR SWITCHING AND CONTROL CIRCUITS ● NPN TRANSISTOREN FÜR SCHALTVORGÄNGE UND REGULATION
70 W Silicon NPN switching power transistor, manufactured using MESA-epitaxy technology, intended for use in switching and control circuits in devices of various uses.
Metal case with two glass isolated passages for base and emitter.
The collector is conductively connected to the housing.
Weight: max. 22 g.
• For sockets covered with solder,
   max. 1.8 mm.
•• It is measured at a distance of
   max. 1.5 mm from the case.
Absolute max limits:	Tc = +25 °C
			KU 607	KU 608
Collector-base voltage	UCBO	max.	210	250	V
Collector-emitter voltage
RBE = 0 Ω	UCES	max.	210	–	V
RBE = 3,9 Ω	UCER	max.	–	250	V
	UCEO	max.	80		V
Emitter – Base Voltage	UEBO	max.	5		V
Collector current	IC	max.	10		A
Emitter current	– IE	max.	12		A
Base current	IB	max.	2		A
Total power loss (Tc ≤ 35 °C; UCE = 0 ... 20 V)	Ptot	max.	70		W
Transition temperature	Tj	max.	+155		°C
Ambient temperature	Ta	max.	–50 ... +50		°C
Internal thermal resistance	Rthjc	max.	1,5		K/W

Characteristic data:	Tc = +25 °C
Nominal values:		nom.	min.–max.
* Collector-base residual current
(UCB = 150 V)	ICBO	0,17	≤1	mA
Collector-emitter residual current
(UCE = 210 V, RBE = 0 Ω) KU 607	ICES	0,9	≤10	mA
(UCE = 250 V, RBE = 3,9 Ω) KU 608	ICER	–	≤20	mA
* Residual emitter current
(UCE = 5 V)	IEBO	0,35	≤10	mA
Current amplification factor
(UCE = 1,7 V, IC = 0,5 A)	h21E	40	≥10
* (UCE = 1,7 V, IC = 8 A)	h21E	50	≥10
Base saturation voltage
(IC = 0,5 A, IB = 0,05 A) KU 607	UBE sat	0,7	≤1	V
(IC = 8 A, IB = 0,8 A)	UBE sat	0,98	≤2,4	V

Note: This translation is based on a direct transcript of the original Czech datasheet. Shown on the next pages are this original datasheet and the initial transcript. Note that the sole purpose of the transcript is to ease any future translation efforts. This transcript and translation does not imply any IP-rights on my behalf, I’ve not done any more that actually transcribe and translate the original document, recreating some graphical elements in the process. So, nothing much really.
Cheers!
Gjermund Skogstad
Norway